Nova Dovetail Chisel

Another quality accessory for the Teknatool Nova Chucks.

Thank you for purchasing the Nova Dovetail Chisel.

For safety reasons, please carefully read and understand these instructions. Use of the Dovetail Chisel incorrectly could cause result in the risk of serious injury.  If you are unsure of the use or the application of this accessory, contact the technical support department of Teknatool International or your reseller.

The Nova Dovetail Chisel is suitable for use with any of the chuck jaws, and does both contractile and expansion cuts to suit the chuck jaws.

USING THE NOVA DOVETAIL CHISEL:

The Nova Dovetail Chisel has been designed for use in several ways.

- Using as a scraper and for cutting the recess of the wood for jaw expansion.

- Used as a cutter in the right hand side of the centre allowing to cut the shape for the jaws in a contraction mode. The Spindle runs in reverse for this operation.

NOTE: Ensure that the workholding device had a side locking screw to secure it to the spindle and is done up. This will avoid the device and work from unwinding from the spindle thread whilst the spindle runs in reverse.

USE THE SCALE TO MARK OUT YOUR WORK

On the HSS stem of the chisel there is a scale which is designed to be used to mark out the diameter you want to cut your dovetail to.

Place the chisel on the face of the work after it has been machined flat, with the CTR (centre) mark in the centre of the work. Use the scale to mark out the dovetail diameter for either 50mm or 100mm diameters.

The 50 mark is for the Nova 50mm, 35 & 45mm Spigot jaws (late model jaws post October 02).

The 100mm mark is for the Nova 100mm jaws and Powergrip jaws.

(Some Notes on Sharpening:

As with many other woodturning tools the Nova Dovetail Chisel must be kept sharp to provide a clean finish. This sharpening can be done using a grinder.